Mono Bluetooth Headset M100C

User Manual

Contents:

1. Product Overview -------------------------------------------------------------------  1

2. Basic Operation  ---------------------------------------------------------------------  2

3. Bluetooth Pairing and Connection    --------------------------------------------  3

4. Connection with Two devices ----------------------------------------------------- 4

5. LED Indicator   ------------------------------------------------------------------------ 5

6.  Charging-------------------------------------------------------------------------------- 6

7. Product Specification     ------------------------------------------------------------ 7

8. Attentions and Q & A  --------------------------------------------------------------- 8

1. Product Overview:

Multi-Function Button (MFB)

Volume + / Next Song

Volume - / Previous Song

Microphone Mute Button & LED Indicator

Type-C Charge Port

Microphone

Package Contents：

A.	Bluetooth Headset BH-M100C x 1

B.	Type-C charge cable x 1

C.	User manual x 1

D.	Type-C to 3.5mm Audio cable x 1

2. Basic Operation:

| Button | Function | Operation Instruction |
| --- | --- | --- |
| MFB | Power On | In off status, long press MFB for 3 seconds to power on (With tone: Power on). M100C will power on and enter paring mode automatically (will enter reconnect mode automatically if have paring record) |
|  | Power Off | In on status, long press MFB for 5 seconds to power off (With tone: Power off). |
|  | Enter Pairing Mode | In off status, long press MFB for 5-7 seconds (With tone: Pairing), or under unconnected standby mode to double press MFB |
|  | Play / Pause | Short press when play music. |
|  | Redial A Call | In connected standby/playing music mode, double press MFB to dial the last call. |
|  | Voice Dialing | In connected standby/playing music mode, long press MFB for 2-3 seconds then release. |
|  | Audio Switch | When during a call, long press for 1 second MFB then release. |
|  | Answer/Hang up/Reject a call | When a call incoming, short press to answer; When during a call, short press to hang up; When a call incoming, long press for 1 second to reject a call. |
| Volume + | Volume Up | Short press. |
|  | Next Song | Long press for 1 second. |
| Volume - | Volume Down | Short press. |
|  | Previous Song | Long press for 1 second. |
| Microphone Mute Button | Microphone Mute | When during a call, short press button to mute, press again to cancel. |
| Audio Cable | Listen to music and phone call | Take the Type-C to 3.5mm audio cable, Type-C end to M100C charge port, 3.5mm end to phone or PC port. |

3. Bluetooth Pairing and Connection:

A. In off status, long press MFB 5-7 seconds to enter pairing mode with LED Blue & Red flash alternately.

B.  Search and click to connect ”M100C” on your phone Bluetooth lists, LED change to Blue slow flash once after connected, now you can play music from phone to headphone.

C. You can press MFB / Volume+ / Volume- / Microphone Mute Button on the Bluetooth headset to control the answer/hang up a call and play/pause of the music, next and previous song, volume up and down, microphone mute.

2 Connection:

Search and click to connect “ M100C” on your phone Bluetooth lists.

1 Pairing:

In off status，Long press MFB 5-7 seconds to enter pairing mode with LED Blue & Red alternately flash.

4. Connection with Two devices:

A. Follow part 3 to connect with first phone, then turn off the Bluetooth function of first phone.

B. The headset will enter pairing mode automatically with Red & Blue LED flash alternately. Turn on the bluetooth function of second phone to search and connect “M100C”, LED change to Blue slow flash after connected.

C. Turn on Bluetooth function of first phone, click to reconnect “M100C”on Bluetooth lists. Headset is connected with two phones now.。

* Music only can be played from one phone under two connections, when you want to play music from another phone, you need to pause or close the music of the previous phone. The same operation during talking status.

5. LED Indicator

| Mode | LED Indicator |
| --- | --- |
| Power on | Blue LED flash 3 times |
| Power off | Red LED is on for 1 second |
| Pairing mode | Red & Blue LED flash alternately |
| Delete pairing record | Blue and Red LED flash once at the same time |
| Reconnect mode | Blue LED flash twice every 5 seconds |
| Unconnected standby mode | Blue LED flash twice every 5 seconds |
| Connected standby mode | Blue LED flash once every 10 seconds |
| Playing Music | LED Blue flash twice every 10 seconds |
| Talking | LED Blue flash twice every 10 seconds |
| Low battery | Red LED flash |
| Charging | Solid Red LED |
| Full charged | Solid Blue LED |

6. Charging

Please charge the M100C at once when the Red LED flash. Charging time is about 1.5 hours. Solid Red LED change to Solid Blue LED when full charged.

Charge Connections

Please connect to the M100C charging port through the Type-C end of Type-C charging cable, USB end to the charger, can be used as car charger, travel charger, computer USB, etc.

Type-C charging cable

Charging with PC

Charging with charger

Note:

1. Please charge the M100C at least one time every 2 months when don’t use it.

2. Charging when power on, headset will be reset and power off.

7. Product Specification:

| Item No. | M100C |
| --- | --- |
| Bluetooth Version | V5.0, Class II |
| Bluetooth Chipset | CSR BC8615 |
| Frequency Range | 2.402GHz-2.480GHz |
| Stand-by Time | About 400 hours |
| Working Time | About 30 hours (70% volume) |
| Charging Time | About 1.5 hours |
| Operation Range | 10 meters |
| Bluetooth Protocols | HSP, HFP, AVRCP, A2DP |
| Two connections (two phones) | Support |
| CODEC Code | SBC |
| Battery Capacity | 420mAh/3.7V |
| Working Temperature | -10—55℃ |
| Headset Net Weight | 141g |
| Headset Dimension | 192.90*157.08*54.05mm |

*Actual use time will differ from environment and music

8. Attentions and Q & A:

A. How to reconnect and operation when failed to reconnect?

When M100C connected with your mobile phone successfully at the first time,  it will search and reconnect the paired device automatically when power on, If failed, please pair and connect again.

B. How to delete paired records?

In power on status, long press the MFB and Volume + Button for 5 seconds to clear the pairing record. The indicator Blue and Red LED flash once at the same time that means the pairing record has been cleared, and the M100C will not connect the connected device. When there are various connection problem, try clearing the pairing record firstly.

C. Power off automatically.

M100C will power off if does not connect any devices for over 5 minutes, or battery voltage is less than 3.1V.

D. Low battery alert.

When battery voltage is less than 3.2V, there will be a tone “Battery Low” every 3 minutes.

E. What’s the password for pairing?

Some connection devices require password for pairing, pls try 0000 or 8888 or 1111  or 1234.

F. What devices could charge for the headphone?

Any car charger, power bank, PC  etc which meet DC 5V , charging current more than 1A could be charge for this item.

G. How to do if have connect issue or dead?

In power on status, plug charging cable for charging, will reset the headset and power off.

H. How to enter paring mode?

In off status, long press MFB for 5-7 seconds to enter paring mode, or under unconnected standby or reconnect mode to double press MFB to enter paring mode. Also will enter paring mode after Bluetooth disconnect.

I. Can be used when charging?

When need to use headset for a long time, because the working time is limited due to the build-in battery, can plug charging power supply (Plug charging cable for charging will reset and power off, need to power on to use), when the battery power is too low or the power supply is poor, it may cause electric current to appear.